ALUMICOR GUIDE NOTE: This master specification section includes ALUMICOR GUIDE NOTEs identified as “ALUMICOR GUIDE NOTE” for information purposes and to assist the specification writer in making appropriate decisions. The ALUMICOR GUIDE NOTE always immediately precedes the text to which it is referring. The section serves as a guideline only and should be edited with deletions and additions to meet specific project requirements.

ALUMICOR GUIDE NOTE: This specification section follows the recommendations of the Construction Specifications Canada, Manual of Practice including MasterFormat(, SectionFormat(, and PageFormat(. Optional text is indicated by square brackets [ ]; delete the optional text including the brackets in the final copy of the specification. Delete the ALUMICOR GUIDE NOTEs in the final copy of the specification. Trade/brand names with appropriate product model numbers, styles and types are used in ALUMICOR GUIDE NOTEs and in the specification text Article or Paragraph titled (Acceptable Material(.

ALUMICOR GUIDE NOTE: This Section is based upon Alumicor Ltd., Storefront FlushGlaze 800, FlushGlaze TL 1800 and BTube 500 Series.

ALUMICOR GUIDE NOTE: When storefront is exposed to exterior weather, Alumicor Ltd., recommends the use of thermally broken systems.  Refer to Alumicor’s master guide specification Section 08 43 13 – Aluminum Framed Storefronts (Thermally Broken).

1	GENERAL

1.01	SUMMARY OF WORK

.1	This Section specifies glazed, non-thermally broken aluminum-framed storefronts and accessories.

1.02	RELATED REQUIREMENTS

ALUMICOR GUIDE NOTE: Include in this Paragraph only those sections and documents that directly affect the work of this section. If a reader of this section could reasonably expect to find a product or component specified in this section, but it is actually specified elsewhere, then the related section number(s) should be listed in the Paragraph below. Do not include Division 00 Documents or Division 01 Sections since it is assumed that all technical sections are related to all project Division 00 Documents and Division 01 Sections to some degree. Refer to other documents with caution since referencing them may cause them to be considered a legal part of the Contract. Edit the following paragraphs to suit specific project conditions.

.1	Section [07 62 00 - Metal Flashing and Trim: Flashings].

.2	Section [07 84 00 – Firestopping: Firestopping insulation].

.3	Section [07 92 00 - Joint Sealing].

.4	Section [08 11 17 – Aluminum Doors: Aluminum-framed glazed swing doors].

.5	Section [08 44 13 – Glazed Aluminum Curtain Walls: Mock-up].

.6	Section [08 51 13 – Aluminum Windows: Mock-up].

.7	Section [08 80 50 – Glazing: Insulating glass units].

ALUMICOR GUIDE NOTE: In the following Article, include only those reference standards which appear in the finished version of the project specification.

1.03	REFERENCE STANDARDS

.1	Aluminum Association (AA)

.1	DAF 45 [2003], Designation System For Aluminum Finishes.

.2	American Architectural Manufacturers Association (AAMA).

.1	AAMA-501-[2005], Methods of Test for Exterior Walls.

.2	AAMA-2603-[2013], Voluntary Specification, Performance Requirements and

Test Procedures for Pigmented Organic Coatings on Aluminum Extrusions and Panels.

.3	AAMA-2604-[2013], Voluntary Specification, Performance Requirements and

Test Procedures for High Performance Organic Coatings on Aluminum Extrusions and Panels.

.4	AAMA-2605-[2013], Voluntary Specification, Performance Requirements and

Test Procedures for Superior Performing Organic Coatings on Aluminum Extrusions and Panels.

.5	AAMA CW-10-[2012], Care and Handling of Architectural Aluminum From Shop to Site.

.6	AAMA CW-11-[1985], Design Windloads for Buildings and Boundary Layer Wind

Tunnel Testing.

.7	AAMA-TIR A1-[2004], Sound Control for Fenestration Products.

.3	ASTM International (ASTM).

.1	ASTM A653 / A653M – [09a], Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process.

.2	ASTM B209-[2010], Specification for Aluminum and Aluminum-Alloy Sheet and Plate.

.3	ASTM B221-[2013], Specification for Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes.

.4	ASTM C612 – [2014], Standard Specification for Mineral Fiber Block and Board Thermal Insulation.

.5	ASTM E283-[2012], Test Method for Determining the Rate of Air Leakage Through Exterior Windows, Curtain Walls, and Doors Under Specified Pressure Differences Across the Specimen.

.6	ASTM E331-[2009], Standard Test Method for Water Penetration of Exterior Windows, Skylights, Doors, and Curtain Walls, by Uniform Static Air Pressure Difference.

.7	ASTM E413 – [04], Classification for Rating Sound Insulation.

.8	ASTM E1105 – [2008], Standard Test Method for Field Determination of Water Penetration of Installed Exterior Windows, Skylights, Doors, and Curtain Walls, by Uniform or Cyclic Static Air Pressure Difference.

.9	ASTM D2240 – [2010], Standard Test Method for Rubber Property—Durometer Hardness.

.4	Canada Green Building Council (CaGBC).

.1	LEED® Canada-NC Version 1.0-[2004], LEED (Leadership in Energy and Environmental Design): Green Building Rating System Reference Package For New Construction and Major Renovations including Addendum 2007.

.5	Canadian General Standards Board (CGSB).

.1	CAN/CGSB-12.8-[97], Insulating Glass Units.

.2	CAN/CGSB-12.20-[M89], Structural Design of Glass for Buildings.

.3	CAN/CGSB-19.13-[M87], Sealing Compound, One-Component, Elastomeric, Chemical

Curing.

.6	CSA International (CSA)

.1	CAN/CSA-S157-[2005], Strength Design in Aluminum.

.2	CAN/CSA-S136–[2007], North American Specification for the Design of Cold-Formed Steel

Structural Members.

.3	CAN/CSA W59.2-[M1991(R2003)], Welded Aluminum Construction.

.7	Environmental Choice Program (ECP)

.1	CCD-45-[1995], Sealants and Caulking Compounds.

.8	Underwriter’s Laboratories of Canada (ULC)

.1	CAN/ULC-S710.1 [2005], Standard for Thermal Insulation – Bead-Applied One Component Polyurethane Air Sealant Foam, Part 1: Materials Standard for Thermal Insulation - Bead - Applied One Component Polyurethane Air Sealant Foam, Part 1: Materials.

1.04	ADMINISTRATIVE REQUIREMENTS

.1	Co-ordination: Co-ordinate work of this Section with work of other trades for proper time and sequence to avoid construction delays.

.2	Pre-installation Meeting: Convene pre-installation meeting after Award of Contract and one week prior to commencing work of this Section to verify project requirements, substrate conditions and coordination with other building sub-trades, and to review manufacturer(s written installation instructions.

.1	Comply with Section 01 31 19 - Project Meetings and co-ordinate with other similar pre-installation meetings.

.2	Notify attendees 2 weeks prior to meeting and ensure meeting attendees include as minimum:

.1	Owner;

.2	Consultant;

.3	Glazing subcontractor;

.4	Manufacturer’s Technical Representative.

.3	Ensure meeting agenda includes review of methods and procedures related to glazed aluminum-framed storefront installation including co-ordination with related work.

.4	Record meeting proceedings including corrective measures and other actions required to ensure successful completion of work and distribute to each attendee within 1 week of meeting.

ALUMICOR GUIDE NOTE: Article below includes submittal of relevant data to be furnished by Contractor.

1.05	ACTION AND INFORMATIONAL SUBMITTALS

.1	Make submittals in accordance with Contract Conditions and Section 01 33 00 - Submittal Procedures.

.2	Product Data: Submit product data including manufacturer’s literature for glazed aluminum aluminum-framed storefront extruded members, panels, components and accessories, indicating compliance with specified requirements and material characteristics.

.1	Submit list on aluminum-framed storefront manufacturer’s letterhead of materials, components and accessories to be incorporated into Work.

.2	Include product names, types and series numbers.

.3	Include contact information for manufacturer and their representative for this Project.

.3	Shop Drawings: Submit drawings stamped and signed by Professional Engineer registered or licensed in [Province] [Territory] of [_____], Canada. Include on shop drawings:

.1	Aluminum-framed storefront panel and component dimensions, framed opening requirements and tolerances, adjacent construction, anchor details anticipated deflection under load, affected related Work, weep drainage network, expansion and contraction joint location and details, and field welding required.

ALUMICOR GUIDE NOTE: Include the following Paragraph for thermally broken aluminum-framed storefront.

.2	Include details of fasteners between interior and exterior extrusions.

ALUMICOR GUIDE NOTE: Include the following Paragraph if project is located in seismically active zone.

.3	Show size and location of seismic restraints. Include seismic design calculations

.4	Samples:

.1	Submit duplicate 300 x 300 mm (12 x 12 inches) sample sections showing prefinished aluminum surface, finish, colour and texture.

.2	Submit duplicate 300 x 300 mm (12 x 12 inches) sample sections of insulating glass unit showing glazing materials and edge and corner details.

.5	Thermal Performance: Submit verification that Insulating Glass Units used in aluminum-framed storefront system meet RSI (R) values specified.

.6	Test Reports:

.1	 Submit test reports showing compliance with specified performance characteristics and physical properties including air infiltration, water infiltration and structural performance.

.7	Field Reports: Submit manufacturer’s field reports within 3 days of manufacturer representatives site visit and inspection.

.8	Sustainable Design (LEED).

.1	LEED Submittals: In accordance with Section [01 35 21 – LEED Requirements]

.9	Installer Qualifications:

.1	Submit letter verifying installer’s experience with work similar to work of this Section.

1.06	CLOSEOUT SUBMITTALS

.1	Operation and Maintenance Data: Supply maintenance data for aluminum-framed storefront for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

ALUMICOR GUIDE NOTE: If LEED is not a part of the project delete the following Paragraph in its entirety.

.2	Sustainable Design Closeout Documentation (LEED).

.1	Provide calculations on end-of-project recycling rates, salvage rates, and landfill rates for work of this Section demonstrating percentage of construction wastes which were recycled.

.2	Submit verification from recycling facility showing receipt of materials.

.3	Record Documentation: In accordance with Section 01 78 00 - Closeout Submittals.

.1	List materials used in aluminum-framed storefront work.

.2	Warranty: Submit warranty documents specified.

1.07	QUALITY ASSURANCE

.1	Sustainability Standards Certification (LEED).

.1	LEED Canada-NC Version 1.0 submittals: in accordance with Section 01 35 21 - LEED Requirements.

ALUMICOR GUIDE NOTE: Consultant may want to construct a Mock-up to establish quality of work for the Project. The Mock-up can be used as a standard to which work on the Project can be compared. If aluminum-framed storefront is to be incorporated into a curtain wall system, co-ordinate the following paragraph with the curtain wall section in the Project Manual. Typically a mock-up is not required for storefronts not included in a curtainwall system. If the aluminum-framed storefront is a “stand-alone” project, delete the following paragraph.

.2	Mock-up: Co-ordinate mock-up of aluminum-framed storefront with Section [08 44 13 – Glazed Aluminum Curtain Wall] [08 51 13 – Aluminum Windows].

ALUMICOR GUIDE NOTE: The following Article although not part of Quality Assurance, can be used to enhance the quality of materials by ensuring that they are delivered and handled properly at the work site.

1.08	DELIVERY STORAGE AND HANDLING

.1	Delivery and Acceptance Requirements:

.1	Deliver material in accordance with Section 01 61 00 - Common Product Requirements.

.2	Deliver glazed aluminum-framed storefront materials and components in manufacturer(s original packaging with identification labels intact and in sizes to suit project.

.2	Material Handling: To AAMA CW-10.

.3	Storage and Handling Requirements: Store materials off ground and protected from exposure to harmful weather conditions and at temperature conditions recommended by manufacturer.

.1	Material storage: To AAMA CW-10.

.4	Packaging Waste Management:

ALUMICOR GUIDE NOTE: For smaller projects that do not have a separate Section for waste management and disposal, delete the following paragraph.

.1	Separate and recycle waste packaging materials in accordance with Section 01 74 19 - Construction Waste Management and Disposal.

.2	Remove waste packaging materials from site and dispose of packaging materials at appropriate recycling facilities.

ALUMICOR GUIDE NOTE: For smaller projects that do not have a Waste Management Plan, delete the option referring to a Waste management Plan.

.3	Collect and separate for disposal paper and plastic material in appropriate on-site storage containers for recycling[ in accordance with Waste Management Plan].

1.09	WARRANTY

.1	Project Warranty: Refer to Contract Conditions for project warranty provisions.

.2	Manufacturer’s warranty: Submit, for Owner’s acceptance, manufacturer’s standard warranty document executed by authorized company official. Manufacturer’s warranty is in addition to and not intended to limit other rights Owner may have under Contract Conditions.

ALUMICOR GUIDE NOTE: Coordinate article below with manufacturer’s warranty requirements only when insulating glass units are used in design.

.3	Warranty period: [1] [2] years commencing on Date of Substantial Performance of Work.

.1	Insulating glass units: [10] years, on Date of Substantial Performance of Work.

2	PRODUCTS

2.01	MANUFACTURER

.1	Manufacturer: Alumicor Limited, 290 Humberline Drive, Toronto, Ontario, Canada M9W 5S2, Phone: (416) 745-4222 or (877) ALUMICOR, e-mail: info@Alumicor.com, URL: www.Alumicor.com.

2.02	DESCRIPTION

.1	Aluminum-framed glazed storefront constructed from prefinished aluminum extrusions and including swing type doors.

ALUMICOR GUIDE NOTE: Choose one of the following two paragraphs to suit project requirements.  .

.2	Storefront Framing: Fin tube framing [101.6] (4 inches) deep.

.1	Aluminum-framed storefront: [44.5] (1.75inches) wide profile.

.3	Storefront Framing: Flush glazed framing 114.3 mm (4.5 inches) deep.

.1	Aluminum-framed storefront: 44.5 mm (1.75 inches) wide profile.

2.03	DESIGN CRITERIA

.1	Design aluminum-framed storefront to [AAMA CW-DG-1].

.2	Design aluminum components to [CAN/CSA S157].

.3	Design and size aluminum-framed storefront to withstand dead and live loads caused by pressure and suction of wind, acting normal to plane of wall using design pressure of [0.95 kPa (20 psf)] to [AAMA CW 11] [ASTM E330].

.1	Design aluminum-framed storefront system for expansion and contraction caused by cycling temperature range of [95] degrees C ([171] degrees F) over [12] hour period without causing detrimental effect to system components.

ALUMICOR GUIDE NOTE: Consideration should be given to the colour of the aluminum-framed storefront system when calculating expansion and contraction since darker colours will have a greater coefficient of expansion than lighter colours.

.2	Thermal expansion: Ensure aluminum-framed storefront system can withstand temperature differential of [85] degrees C ([153] degrees F) and is able to accommodate interior and exterior system expansion and contraction without damage to components or deterioration of seals.

.3	Design vertical expansion joints with baffled overlaps and compressed resilient air seal laid between mullion ends.

.4	Ensure system is designed to accommodate:

.1	Movement within aluminum-framed storefront assembly.

.2	Movement between system and perimeter framing components.

.3	Dynamic loading and release of loads.

.4	Deflection of structural support framing.

.5	Shortening of building concrete structural columns.

.6	Creep of concrete structural members.

.7	Mid-span slab edge deflection: [______] mm maximum.

ALUMICOR GUIDE NOTE: Use the following paragraph only when storefront is exposed to exterior weather conditions.

.5	Thermal resistance:

ALUMICOR GUIDE NOTE: The RSI or R value for the glass areas of the aluminum-framed storefront is totally dependent not only on whether a double or triple pane Insulating Glass Unit (IGU) is used, but also upon the manufacturer of the IGU. Check the IGU manufacturer’s technical literature before specifying the RSI or R values.

.1	Vision glass areas: Insulating Glass Unit [RSI [______] (R [______])].

.6	Limit mullion deflection to [flexure limit of glass [19] mm (0.75 inches)] [L/175] [L/200] [L/240] maximum with full recovery of glazing materials.

ALUMICOR GUIDE NOTE: Check with local authority having jurisdiction to determine local STC rating requirements.

.7	Sound attenuation through storefront system (exterior to interior): STC [33] to [AAMA T1R - A1] [ASTM E413].

.8	Glass dimensions: Size glass units to CAN/CGSB-12.20.

.9	Flatness criteria: [6] mm ([0.25] inches) maximum in [6] m (20 feet) for each panel.

ALUMICOR GUIDE NOTE: When storefront is exposed to exterior weather, Alumicor Ltd., recommends the use of thermally broken systems.  Refer to Alumicor’s master guide specification Section 08 43 13 – Aluminum Framed Storefronts (Thermally Broken).

ALUMICOR GUIDE NOTE: Use the following six paragraphs only when storefront is exposed to exterior weather conditions.

ALUMICOR GUIDE NOTE: Air infiltration in both the AAMA 501 and ASTM E283 standards are measured in m3/s/m2 in lieu of the preferred designation of l/s/m2. Refer to CSC TEK.AID 07195 - Air Barriers for discussion on air infiltration. In Canada the recognized SI Metric unit of measurement is the litre (L) and is used in this specification. There are 1,000 litres in a cubic metre.

.10	Air infiltration: [0.3] L/s/m2 ([0.63] cfm) maximum of wall area to [AAMA 501] [ASTM E283] at differential pressure across assembly of [300] Pa (0.044 psi).

.11	Water infiltration: None to [AAMA 501] [ASTM E331] [ASTM E1105] at differential pressure across assembly of [720] Pa (0.104 psi).

.12	Ensure interior surfaces have no condensation before exposed edges of sealed units reach dew point temperatures during testing to [AAMA 501].

.13	Maintain continuous air barrier and vapour retarder throughout building envelope and aluminum-framed storefront assembly.

.14	Ensure no vibration harmonics, wind whistles, noises caused by thermal movement, thermal movement transmitted to other building elements, loosening, weakening, or fracturing of attachments or components of system occur.

.15	Reinforce aluminum-framed storefront system to accommodate window washing guide rails where indicated.

2.04	MATERIALS

.1	Aluminum-Framed Storefront System and Components:

.1	Extruded aluminum: To ASTM B221, 6063 alloy with [T5] [T6] temper.

.2	Sheet aluminum: To [ASTM B209], utility grade for unexposed surfaces.

.3	Fasteners, screws and bolts: Cadmium plated stainless steel [300] [or] [400] series to meet aluminum-framed storefront requirements and as recommended by manufacturer.

.4	Anchors: Ensure anchors have three-way adjustment.

.5	Aluminum panels: [3] mm (0.125 inches) thick factory formed panels.

.1	Finish after forming to match [window] [curtain wall] system.

ALUMICOR GUIDE NOTE: Use the following paragraphs only when storefront is not exposed to exterior weather conditions and single glazing is included in the design. Delete the paragraph if insulating glass units are used..

.6	Vision glass: [6] mm ([0.25] inches) clear float glass.

ALUMICOR GUIDE NOTE: Use the following two paragraphs only when storefront is exposed to exterior weather conditions.

Alumicor Guide Note: Retain the following paragraphs if insulating glass units are specified in another Section. Delete the paragraph if they are specified here.

.7	Insulating glass units: In accordance with Section [08 80 50 – Glazing].

.8	Insulating glass units: To [CAN/CGSB-12.8], double glazed, hermetically sealed, argon filled insulating glass units with low conductance [black] stainless steel warm edge spacer.

.1	Outer lite: [6] mm ([0.25] inches) clear [float] [tempered] glass with low-E coating on surface two.

.2	Inner lite: [6] mm ([0.25] inches) clear [float] [tempered] glass

Alumicor Guide Note: Retain the following paragraphs if aluminum-framed doors are specified in another Section. Delete the paragraph if they are specified here.

.9	Doors: In accordance with Section [08 11 17 - Aluminum Doors].

.10	Doors: Aluminum-framed swing door with glass insert suitable for inclusion in aluminun-framed storefront system, constructed and finished to match storefront.

Alumicor Guide Note: Co-ordinate the following paragraph with door type specified in Section 08 11 17 – Aluminum Doors.

.1	Acceptable material: Alumicor Ltd., [Canadiana] [Canadiana HD] [Insuldoor].

ALUMICOR GUIDE NOTE: When storefront is exposed to exterior weather, Alumicor Ltd., recommends the use of thermally broken systems.  Refer to Alumicor’s master guide specification Section 08 43 13 – Aluminum Framed Storefronts (Thermally Broken).

Alumicor Guide Note: Choose the Alumicor Ltd., Storefront that best meets the project requirements. B-Tube 500 Series uses the 101.6 mm (4 inch) frame all other Series use the 114.3 mm (4.5 inch) frame.

.2	Acceptable Material: Alumicor Ltd.,  [B-Tube 500] [FlushGlaze 800] [FlushGlaze 1800] Series Storefront.

2.05	aluminum-framed storefront system FABRICATION

.1	Do aluminum welding to CAN/CSA W59.2.

.2	Fabricate aluminum assemblies of extruded sections to sizes and profiles indicated.

.1	Ensure verticals and horizontals are extrusions designed for either shear block or screw spline corner construction.

.3	Construct units square, plumb and free from distortion, waves, twists, buckles or other defects detrimental to performance or appearance.

ALUMICOR GUIDE NOTE: When storefront is exposed to exterior weather, Alumicor Ltd., recommends the use of thermally broken systems.  Refer to Alumicor’s master guide specification Section 08 43 13 – Aluminum Framed Storefronts (Thermally Broken).

ALUMICOR GUIDE NOTE: Use the following paragraph only when storefront is exposed to exterior weather conditions.

.4	Fabricate aluminum-framed storefront with minimum clearances and shim spacing around panel perimeter and ensure installation and dynamic movement of perimeter seal is enabled.

.5	Fabricate infill panels with metal covered edge seals around perimeter of panel assembly, enabling installation and minor movement of perimeter seal.

.6	Fabricate aluminum framed doors in accordance with Section [08 11 17 – Aluminum Doors].

.7	Accurately fit and secure joints and corners.

.1	Ensure joints are flush, hairline, [and weatherproof].

.8	Prepare aluminum-framed storefront to receive anchor devices.

.9	Use only stainless steel or zinc plated concealed fasteners

.1	Where fasteners cannot be concealed, countersunk screws finished to match adjacent material may be used upon receipt of written approval from Consultant.

ALUMICOR GUIDE NOTE: Co-ordinate the following paragraph with the drawings to ensure that automatic entrances, revolving doors, storefront and other doors are adequately indicated.

.10	Prepare components to receive doors and openings as indicated.

ALUMICOR GUIDE NOTE: Co-ordinate the following paragraph with the drawings to ensure that such things as window cleaning equipment are adequately indicated.

.11	Reinforce framing members for exterior imposed loads where required.

.12	Visible manufacturer’s labels are not permitted.

2.06	FINISHES

ALUMICOR GUIDE NOTE: Choose one of the following three paragraphs to specify the finish on exposed aluminum  surfaces.

.1	Exposed aluminum surfaces: To [AAMA 2604, 2-coat, thermal setting enamel consisting of primer and topcoat] [AAMA 2605, 3-coat, thermal setting enamel consisting of primer, colour coat and clear coat] with [70] % minimum fluoropolymer resin and polvinyldiene fluoride (PVDF)], [0.025 mm (1 mil)] [0.03 mm (1.2 mil)] minimum total thickness coloured [______].

ALUMICOR GUIDE NOTE: Duranar XL is a thicker more durable finish than Duranar. Some colours such as metallics are only available as Duranar XL finishes.

.1	Acceptable material; PPG Industries Inc., [Duranar] [Duranar XL].

ALUMICOR GUIDE NOTE: For Alumicor products, Class 1 is available in Clear, Champagne, Light Bronze and Black. Class II is only available as a Clear anodized finish.

.2	Exposed aluminum surfaces: To AA DAF-45-M10C21[A41][A44], Architectural Class I, anodized [18 µm (0.0007 inches)] minimum thickness coloured [clear][______].

.1	Acceptable material: Alumicor Ltd., Class I Anodic Finish.

.3	Exposed aluminum surfaces: To AA DAF-45-M10C21A31, Architectural Class II, clear anodized [10 µm (0.0004 inches)] minimum thickness.

.1	Acceptable material: Alumicor Ltd., Class II Anodic Finish.

2.07	ACCESSORIES

ALUMICOR GUIDE NOTE: The application of caulking releases volatile organic compounds (VOCs) into the atmosphere. VOCs contribute to numerous environmental problems including the degradation of indoor air quality, the formation of ground level ozone and photochemical smog. The specification of caulking and sealants that have a low VOC content and reduced toxicity will help to protect the environment and reduce possible adverse health effects. The specification of products that are certified to meet the specification of the Environmental Choice Program CCD-45 will provide reduced environmental impacts. The use of lower VOC products contributes more towards LEED credits.

.1	Gasketing: To [CCD-45] Silicone compatible rubber or extruded silicone gaskets.

.2	Setting Blocks: To [CCD-45] and [ASTM D2240], [neoprene] [EPDM] [silicone], [80 - 90] Shore A Durometer hardness.

.3	Spacers: To [CCD-45] and [ASTM D2240], [neoprene] [EPDM] [silicone], [50 - 60] Shore A Durometer hardness.

.4	Sealant: To [CAN/CGSB-19.13], Class 40, one-component, cold-applied, non-sagging silicone.

.1	Acceptable material: Dow Corning 795.

.5	Sealant Bond Breaker: Open cell foam backer rod sized to suit project requirements.

.6	Flashings: [3] mm (0.125 inches) thick aluminum flashing to profiles indicated [and in accordance with Section 07 62 00 - Sheet Metal Flashing and Trim].

.7	Liquid Foam Insulation: Single component, moisture cure, low expansion rate spray-in-place polyurethane liquid foam insulation to ULC-S710.1 and in accordance with manufacturer’s written recommendations.

2.07	PRODUCT SUBSTITUTIONS

.1	Substitutions: [In accordance with Section 01 23 13 - Product Substitution Procedures] [No substitutions permitted].

2.	Ensure components come from one manufacturer.

3	EXECUTION

3.01	INSTALLERS

Alumicor Guide Note: Alumicor authorized installers use only Alumicor manufactured or approved components. Other installers may substitute other manufacturer’s materials.

.1	Use only [Alumicor authorized installers for] [installers with 2 years minimum experience in work similar to] work of this Section.

3.02	EXAMINATION

.1	Verification of Conditions: Verify that conditions of substrate previously installed under other Sections or Contracts are acceptable for aluminum-framed storefront installation in accordance with manufacturer’s written instructions.

.1	Visually inspect substrate in presence of Consultant.

.2	Inform Consultant of unacceptable conditions immediately upon discovery.

.3	Proceed with installation only after unacceptable conditions have been remedied and after receipt of written approval to proceed from Consultant.

ALUMICOR GUIDE NOTE: When storefront is exposed to exterior weather, Alumicor Ltd., recommends the use of thermally broken systems.  Refer to Alumicor’s master guide specification Section 08 43 13 – Aluminum Framed Storefronts (Thermally Broken) and their installation.

3.03	INSTALLATION

.1	Install aluminum-framed storefront in accordance with manufacturer’s written recommendations.

.2	Do aluminum welding to CAN/CSA W59.2.

.3	Attach aluminum-framed storefront assemblies to structure plumb and level, free from warp, and allow for sufficient adjustment to accommodate construction tolerances and other irregularities.

.1	Maintain dimensional tolerances and align with adjacent work.

.2	Use alignment attachments and shims to permanently fasten elements to building structure.

.3	Clean welded surfaces and apply protective primer to field welds and adjacent surfaces.

ALUMICOR GUIDE NOTE: Use the following two paragraphs only when storefront is exposed to exterior weather conditions.

.4	Install thermal isolation where components penetrate or disrupt building insulation.

.5	Install sill flashings.

.6	Install smoke sealing in accordance with Section [07 80 00 – Fire and Smoke Protection] where indicated.

ALUMICOR GUIDE NOTE: Use the following five paragraphs only when storefront is exposed to exterior weather conditions.

.7	Co-ordinate attachment and seal of perimeter air barrier in accordance with Section [07 27 00 – Air Barriers].

.8	Co-ordinate attachment and seal of perimeter vapour retarder in accordance with Section [07 26 00 – Vapour Retarders].

.9	Install [fibrous insulation] [liquid foam insulation] in shim spaces at perimeter of assembly to maintain continuity of thermal barrier.

.10	Install insulating glass units and infill panels in accordance with Section [08 80 50 - Glazing] and to manufacturer’s written instructions.

.11	Install perimeter sealant [to method required to achieve performance criteria, backing materials, and installation criteria in accordance with Section [07 92 00 - Joint Sealing].

3.04	FIELD QUALITY CONTROL

.1	Field  Inspection: Coordinate field  inspection in accordance with Section [01 45 00 - Quality Control].

.2	Site Installation Tolerances:

.1	Variation from plumb: [12 mm per 30 m (0.5 inches per 100 feet)] maximum.

.2	Misalignment of two adjacent panels or members: [0.8 mm (0.03 inches)] maximum.

.3	Sealant space between aluminum-framed storefront and adjacent construction: [13 mm (0.5 inches)] maximum.

ALUMICOR GUIDE NOTE: Specify requirements if manufacturers are to provide field quality control with onsite personnel for instruction or supervision of product installation, application, erection or construction. Manufacturer field reports are included under PART 1, Action and Informational Submittals.

.3	Manufacturer’s Services:

ALUMICOR GUIDE NOTE: Use the following Paragraphs only when manufacturer’s technical support and assistance services are required to help assess the suitability of product application and the quality of the fabricated and/or installed components. Establish the nature, number and duration of the technical services to be provided by the manufacturer and specify below. Consult the manufacturer for services required. Delete if field services are not required.

.1	Coordinate manufacturer’s services with Section [01 45 00 - Quality Control].

.2	Submit to Consultant a written agreement from the manufacturer to perform the manufacturer’s services.

.3	Schedule manufacturer’s review of work procedures at stages listed:

- Product Application: [1] off site review[s].

- Fabrication and Handling: [1] review[s] at authorized installers fabrication facilities.

- Installation: [3] site reviews at [commencement of Work] [50% completion of Work] [Upon completion of Work].

.4	Submit manufacturer’s written reports to Consultant describing:

.1	The scope of work requested.

.2	Date, time and location.

.3	Procedures performed.

.4	Observed or detected non-compliances or inconsistencies with manufacturers’ recommended instructions.

.5	Limitations or disclaimers regarding the procedures performed.

.6	Obtain reports within seven days of review and submit immediately to Consultant.

3.05	CLEANING

ALUMICOR GUIDE NOTE: For smaller projects that do not have a separate Division 01 Section for cleaning, delete the reference to Section 01 74 00 – Cleaning in the following two Paragraphs.

.1	Progress Cleaning: Perform cleanup as work progresses [in accordance with Section 01 74 00 - Cleaning 	and Waste Management].

.1	Leave work area clean end of each day.

.2	Final leaning: Upon completion, remove surplus materials, rubbish, tools, and equipment [in accordance 	with Section 01 74 00 – Cleaning and Waste Management].

.3	Waste Management:

.1	Co-ordinate recycling of waste materials with 01 74 19 - Construction Waste Management and Disposal.

.2	Collect recyclable waste and dispose of or recycle field generated construction waste created during construction or final cleaning related to work of this Section.

.3	Remove recycling containers and bins from site and dispose of materials at appropriate facility.

3.06	PROTECTION

.1	Protect installed products and components from damage during construction.

.2	Repair damage to adjacent materials caused by aluminum-framed storefront installation.

END OF SECTION 08 43 13 - aluminum-framed storefronts (Non-thermally broken)